## Slide 1
<number>
EDUCATION COVER PAGE
NAME OF EDUCATION : EMERGENCY FIRE DRAIN
TOTAL PAGE NUMBER: 25 PAGE
APPROVAL :

## Slide 2
<number>
Combustible
Heat
Oxygen
The conditions for the combustion process can be

## Slide 3: Fire
<number>
Combustion may to be
It is essential to meet
Combustible – heat– oxygen
This is the path that should be followed in fire fighting will be to disrupt the triangle.
The use of the terms used to fight fire extinguisher is very simple and very effective.

## Slide 4: Fire extinguishers
<number>
Carbon dioxide type
Dry Chemical Powder
Foam

## Slide 5: Fire Fighting Equipment
<number>
Carbon dioxide type fire extinguishers
** The liquid in the tubes of carbon dioxide from the outlet tube - served 80 degrees and is intended for the cooling and was stopped the oxygen at the same time, very effective a fire-fighting equipment.
** Caution should be
Do not touch your hand to the outlet tube.
Definitely not aim at people.
** Use of remote gives positive results maximum of 1 meter or 50 cm from the starting point of a fire.

## Slide 6: Fire fighting equipment
<number>
Dry Chemical Powder type fire extinguishers
** Located in cutting off the oxygen chemical powder fire extinguisher is working towards a fighting equipment.
** Used in all kinds of fire excluding liquid chemicals.
** Fire up to 5 meters away from the starting point gives effective results.

## Slide 7: Fire fighting equipment
<number>
Foam-type fire extinguishers, liquid chemicals in extinguishing the fire extinguishers are allowing the spread without pressure for dispersion.
İs the type of extinguishers for terminating oxygen quencher.

## Slide 8: Fire fighting equipment
<number>

## Slide 9: Fire extinguishing system equipment
<number>

## Slide 10: Fire system equipment
<number>

## Slide 11
<number>

## Slide 12
<number>
FIRE-FIGHTING INSTRUCTIONS FOR USE PORTABLE DEVICES
1. Fire extinguishers have in place, go to the scene of the fire, in the direction of the wind (backed by the wind) into flames 3 - 5 m, until it approached,
2. Pull the pin that secures the trigger,
3. And removing the hose over the launch of the flames at the start, hold,
4. Quickly press the trigger firmly,
5. Right or left by moving the lance of the powder makes contact with each side of the fire,
6. Fire front to back, from below upwards put scans,
7. Fuel flowing or dripping intervention in fire from the top down,
8. If the fire is greater, not more than one consecutive portable extinguishers, used together at the same time,
9. Be wary of reignition, if there are ember wastes put out completely with water cooling,
10. Don’t put into place the used extinguishers without filling.

## Slide 13
<number>
YANGIN TAHLİYE PROSEDÜRÜ
FIRE EVACUATE PROCEDURE
Bir duman veya yangın gördüğünüzde en yakın alarm butonunu çekiniz ve “YANGIN VAR” diye bağırarak başka kişi veya kişilere haber veriniz.
Yangın Alarmı
When you see smoke or fire, pull the nearest alarm button and "FIRE shouting" please inform another person or persons.
Fire Alarm
Notes: <number>

## Slide 14
<number>
İşinizi bırakın, makine ve hatları durdurun. Acil durum organizasyonunda görevli değilseniz tahliye olun, görevli iseniz acil durum toplanma bölgelerine gidin.
Yangın alarmını duyduğunuzda
When you hear a fire alarm
Leave your job, stop the machine and lines. If you are not involved in the organization of emergency you must evacuated, if you emergency officials go to the assembly area.
Notes: <number>

## Slide 15: Tahliye esnasındaki davranışlar What to do during evacuation
<number>
Yangın alarmında aşağıdaki gibi davranmalısınız;
İşinizi bırakın, çalıştığınız makineleri durdurun, şalterleri kapatın, aydınlatmaları ve bilgisayarları kapatın.
Yanan sigaranızı söndürün.
En kısa zamanda bulunduğunuz yeri terk edin.
Sakin olun,koşmayın.
Fire alarms should behave like the following;
Leave your job, you are trying to stop the machine, turn off the switch, lighting and turn off the computer.
Extinguish a burning cigarette.
Leave your place immediately.
Dont’t run and be calm.
Notes: <number>

## Slide 16
<number>
. En yakın ve müsait YANGIN ÇIKIŞ KAPISI 'n dan dışarı çıkın .Turnikeli çıkış kapıları yakınındaysanız ve herhangi bir tehlike söz konusu değilse bu kapıları çıkış için kullanarak bina dışına çıkabilirsiniz. Büyük otoparkın girişinde, tabelalarla belirtilmiş bulunan kart okuyucuya kartınızı sayım için okutun. Departmanlar için ayrılan özel bölgede toplanın (ekli krokide gösterilen).
Leave the building from the the nearest to you fire exit door. İn case you close to normal exit´s and there is no danger, you can also use normal exits
On the entrance of large car park, signposted those indicated in the card reader to read your card counting.
Collected in special areas set aside for the Department's (as shown in the attached sketch).
Notes: <number>

## Slide 17: Toplanma Bölgesi / Meeting Point
<number>
Notes: <number>

## Slide 18
<number>
Toplanma Bölgesi / Meeting Point

## Slide 19: Toplanma Bölgesi / Meeting Point
<number>
Notes: <number>

## Slide 20
<number>
Tehlikenin tamamen geçtiği ilgili yetkililerce bildirilinceye kadar bekleyin.
Tehlike bittiğinde acil durum grup şefinin talimatıyla güvenlik tarafından
“TEHLİKE BİTTİ” sireni çaldırılır.
Wait till issued by the relevant authorities of the danger completely.
When the danger is over, "DANGER OVER" siren will ring by security instruction of the emergency group chief
Notes: <number>

## Slide 21
<number>
Güvenlik personeli tahliye sırasında kimlerin bina içinde kalıp kalmadığını ya da departmanlarında çalışan herkesin toplanma noktasında olup olmadığını kartlı geçiş sisteminden rapor alarak kontrol edeceklerdir. Bu nedenle herkes kendi kartı ile giriş çıkış yapması gerekmektedir.
Security personnel who during the evacuation of the buildings that remain in or rallying point for everyone working in the departments of whether the access control system will control by the report. Therefore, everyone must enter and exit with their card.
Notes: <number>

## Slide 22: Kol aşağı çekildiğinde kilitlenir, kesinlikle kapanmaz. Alarmı susturmak için anahtarla kilit çözülür.
<number>
Yangın alarm butonu / Fire Alarm Button
When down, arms locked, definitely not closed. To silence the alarm key and the lock is released.
Notes: <number>

## Slide 24
<number>

## Slide 25
<number>
Click here for Exam
Notes: <number>